## Slide 1
Master Thesis Defense
Author : Jihad Alsamarji
Design and Control of a Ball and Plate Didactic Device
Supervisor : Prof. Dr. Ir. Micheal Kinnaert
Ir. Laurent Catoire
Co-supervisor : Dr. Ir. Christoph Mertens

## Slide 2
Notes: Control system design is one of the hardest courses taught in engineering.
It has myriad of applications in mechanical,electrical,biomedical and many other disciplines.
One of the reasons why this course is hard for some students is that this sector contains so much maths which is abstract.

## Slide 3
Plant Selection
- Portable
- Safe
- Affordable
- Controllable
- Scalable
- Convenient
2DOF
3DOF
6DOF
Notes: Control system design is one of the hardest courses taught in engineering.
It has myriad of applications in mechanical,electrical,biomedical and many other disciplines.
One of the reasons why this course is hard for some students is that this sector contains so much maths which is abstract.

## Slide 4
Conceptual Design
Sensor
Actuator
Processing Unit
Camera
Resistive Touchscreen
Step Motor
Servo Motor
Arduino
RasberryPi
Custom Made PCB
Computer
Notes: Control system design is one of the hardest courses taught in engineering.
It has myriad of applications in mechanical,electrical,biomedical and many other disciplines.
One of the reasons why this course is hard for some students is that this sector contains so much maths which is abstract.

## Slide 5
Mechanical Design
Size of the actuated plate (30x30cm)
Height of the actuated plate (27cm)
Size of the supporting bench (50x30cm)
Size of the servo frame (Standard Size)
Material and thickness for plate and bench (4mm Plywood)
Material for actuating rods and Camera Support (Carbon fiber)
Material for Additional Supporting structure (PLA 3d printed)
Connection between Rods and Servo Arm (Rod End Bearing or Rocker Ball Joint)
Connection between Rods and Plate (Universal Joint or Magnetic Ball Joint)
Ratio K = dc / dm
Flexibility and customization using slideways.
Using a ball of 0.1 [Kg,] and assuming a critical situation that the plate is handled by one servo motor. The required torque is then roughly speaking 0.42 [Kg.cm]. A customizability factor of 2 is used. To ensure that the servo motor operates in the Continuous region, a rule of thumb is to use a 10x multiplier. Hence the required torque is now 8.4 [Kg.cm].
Accuracy and Response Speed

## Slide 6
Electrical Design

## Slide 7
Software Design
Lookup Table

## Slide 8
Software Design
Notes: The lookup table is to map between the angle theta and alpha since the relation between them is non linear and we don’t want to solve for it analytically each cycle

## Slide 9
Modelling

## Slide 10
System Dynamics Modelling
Equation of motion of the Ball Obtained By LaGrange formulation :

## Slide 11
System Dynamics Modelling
Equation of motion of the Servo motor obtained by second order assumption :
Needs Validation !
Determine parameters by identification !

## Slide 12
System Identification : Servo Motor Dynamics

## Slide 13
System Identification : Servo Motor Dynamics

## Slide 14
System Identification : Servo Motor Dynamics

## Slide 15
System Identification : Servo Motor Dynamics

## Slide 16
System Dynamics Modelling
Need a third equation to link Alpha to Theta !

## Slide 17
System Dynamics Modelling

## Slide 18
System Dynamics Modelling

## Slide 19
System Dynamics Modelling

## Slide 20
System Dynamics Modelling

## Slide 21
LTI State Space Model

## Slide 22
System Dynamics Modelling
Alpha < 15
Alpha > 15

## Slide 23
Control Design

## Slide 24
Control System Design
- States of equilibrium
- Stability analysis
- Controllability Analysis
- Observability Analysis
Interesting to check
Not BIBO Stable
Controllable
Observable

## Slide 25
Control Requirements
Pole Placement
Loop shaping

## Slide 26
Root Locus with No Controller

## Slide 27
Root Locus with ( PD with low pass filter)

## Slide 28
Step Response with ( PD with low pass filter)

## Slide 29
Discrete Simulink Model

## Slide 30
Step Response on Discrete Simulink Model

## Slide 31
Controller Saturation

## Slide 32
Step Response on Discrete Simulink Model

## Slide 33
Validation

## Slide 34
Step Response Validation

## Slide 35
Different PD Controllers Comparison

## Slide 36
Sinusoidal Reference

## Slide 37
Thank You For Your Attention
Questions ?